## Slide 1: RAIN RATE ESTIMATION FROM DUAL POLARISATION RADAR OBERVATIONS Anthony Illingworth University of Reading, UK
23 October 2005
Albuquerque, New Mexico.
AMS Education Forum
With acknowledgements to Robert Thompson of U of Reading

## Slide 2: 1. Why is it difficult to obtain reliable rain rates from Z alone? 2. Define dual polarisation parameters. ZDR, DP|KDP hv, and LDR - using simple dipole explanation. 3. Accuracy of the dual polarisation parameters. 4. Use of Z, ZDR and DP|KDP for more accurate rainfall estimates + errors for data assimilation 5. Unwanted backscatter and attenuation. C-band and X-band radars. 6. Conclusions.
OUTLINE

## Slide 3: 1.Difficulties in finding R from Z alone: Empirical: Z = a Rb (e.g. Z= 300 R1.4, Nexrad)
Ground clutter. Anomalous Propagation, birds, insects, aircraft….
Uncertainty in Z calibration.
Z-R relations changes for different raindrop size spectra.
IS THE BEAM FILLED WITH RAIN?
100km range: 1beam - 2km wide: 200km range, earth curvature >3km.
SUMMER TIME - <100km range. Should be in the rain.
Could have some hail. (Big Z, but often low R).
WINTER TIME – VERTICAL PROFILE OF Z.
Bright band – Z is high in melting snow. (>Z(rain))
Low Z in the dry ice above the melting layer < Z(rain). CHANDRA

## Slide 4: Physical origin of Z-R relationships.
Assume exponential drop size spectrum.
N(D) = No exp(-3.67D/D0): D0 is median volume diameter
R = /6 N(D) D3 V(D) dD = p N 0 D3.67 exp(-3.67D/D0) dD (if V(D)D0.67)
= q N0 D04.67 (1)
Z = N(D) D6 dD = N0 D6 exp(-3.67D/D0) dD
= r N0 D07 (2)
Eliminate D0 from (1) and (2): Z = s (N0 /N07/(4.67)) R7/4.67 (q, r, s constants)
but 7/4.67 = 1.5 so: Z = s (1/ N0) R1.5 = a R b
So ‘a’ varies as (1/ N0) and b = 1.5 if N0 is not a function of D 0.
tropical rain: N0 increases as D0 b = 1.4
stratiform rain, melting snow N0 decreases as 1/D0 : b = 1.63

## Slide 5: EVALUATING RADAR RAINFALL RATES.
What is our specification? Let’s aim for R to 25% (1dB).
Traditionally done with hourly gauge totals.
BUT WHAT ABOUT THE SPATIAL AND TEMPORAL VARIABILITY OF RAINFALL?
Gauge measures at a point – but radar a volume.
Wind drift – how high is the radar beam over the gauge?
How often does a radar need to scan over the gauge in one hour?
Ideally need a scan every 2.5 minutes,
Scan every 5 mins - error typically 20%.
Scan every 15 minutes - error typically 40%, very poor.
QUESTION: SO EVEN IF THE RADAR MEASURES THE RAINFALL PERFECTLY IT MAY NOT AGREE WITH THE GAUGE?

## Slide 6: EXAMPLES FROM TWO POLARIMETRIC STUDIES
Brandes et al (JAM, 2002) Florida.
R(Z) rms error 7.8 mm; with polarisation, R(POL) - rms error 6.7 mm
Ryzhkov et al (JAM 2005, BAMS, 2005) ‘JPOLE’ in Oklahoma.
42 gauges, 50 hours data, mean hourly gauge rainfall 6.3 mm (lots of hail).
R(Z) R(POL)
rms error each gauge NEXRAD Z = 300 R1.4 5.30mm 3.06mm
rms error each gauge ‘tuned’ Z = 527 R1.41 4.05mm 3.06mm
rms error of average gauge rainfall (300R1.4) 2.59mm 1.09mm
Spring hail
Winter stratifrom
Question: Improvement only because hail rejected?

## Slide 7: 2. DUAL POLARISATION PARAMETERS: ZDR , DP|KDP, hv, and LDR - using a simple dipole explanation
Transmit simultaneous H and V polarised signals returns:
i.e. wave linearly polarised at 45 degrees.
Receive amplitude and phase of H and V polarised returns
Initially S-band, 10cm wavelength
Mostly Rayleigh scattering
Mostly negligible attenuation.
For brevity ‘B&C’ will refer to the book:
Bringi and Chandrasekhar, 2001, CUP p636,

## Slide 8: .
1mm
3mm
5mm
Compare Z observed with horizontal and vertically polarised radiation
ZDR = 10 log(ZH/ZV)
the magnitude of ZDR (a ratio)
gives the mean drop size, D0
‘ Z = N D6 ’, knowing D0,
then Z will give us N0 the concentration.
RAIN
ZDR: DIFFERENTIAL REFLECTIVITY
Measures mean shape of hydrometeors.
QUESTION: What if hail present?
HAIL TUMBLES AS IT FALLS
ZH = Z V ZDR = 0dB;
Hail/rain mixture lowers ZDR
- so what is the apparent R?

## Slide 9: DIFFERENTIAL PHASE SHIFT DP
As the H wave propagates through oblate raindrops it lags more and more behind the V wave and a phase difference, DP builds up
The gradient of, DP with range is the specific differential phase shift, KDP, measured in degrees per km. KDP is a measure of R.
HAIL – Tumbles as it falls, delays H and V waves the same, does not contribute to KDP, which responds only to the rain!
KDP depends only on phase, unaffected by calibration errors.

## Slide 10: CHILBOLTON DATA: ZDR AND DP IN RAIN
Z >40dBZ
In heavy rain
ZDR>2dB
In heavy rain
Total phase shift
40 thru
heavy rain

## Slide 11: CO-POLAR CORRELATION COEFFICIENT: hv. The correlation between simultaneously-measured backscattered amplitudes AH and AV over N successive pulses. If all the particles are the same shape, then ratio AH / AV constant and hv =1. hv < 1 tells you that there is a mixture of shapes present.
Target: two spheres and two oblate spheroids. Add up the individual scattering amplitudes ah and av to give resultant amplitudes AH and AV.
As particles reshuffle relative phases
change

## Slide 12: Spheres ‘1’ & ‘2’ backscatter amplitudes ah= av Oblates ‘3’ & ’4’ ah = 2 av
As the particles reshuffle the relative phases change and the resultant amplitudes AH, AV do not quite fluctuate together.
HV< 1
t=0 AH > AV
ZH > ZV
Later time AH = AV
t=t ZH = ZV

## Slide 13: LDR: LINEAR DEPOLARISATION RATIO.
LDR in the rain <30dB: low (<-25dB) in dry ice;
Highest values (>-15dB) in the bright band – use to identify?
- wet melting ice which rocks and rolls as it falls
Transmit Horizontal: Receive Vertical – cross polar return.
LDR = 10 log (cross-polar/co-polar). Difficult for 45  transmission.
NO cross polar
Cross polar return

## Slide 14: Two spheres ‘1’ & ‘2’ backscatter amplitudes ah= av Two oblates ‘3’ & ’4’ ah = 2 av : HV < 1
ah/av not constant so as particles reshuffle
ZDR and dP change.
t=0
ZH> ZV: ZDR>>0dB
DP <0
Later time t=t
ZH =ZV : ZDR = 0dB
DP =0
3. Accuracy of the radar estimates of ZDR& DP

## Slide 15: Accuracy of the radar estimates of ZDR & DP
If HV = 1 then no uncertainty - need JUST ONE RADAR PULSE!
In reality, HV < 1 :
H and V pulse volumes mismatched
e.g. 1% mismatch, max HV = 0.99
Mixture of drop shapes in rain, so max HV  0.98.
Uncertainty is random, reduce with many independent samples.
NEXRAD. Typical spec (Ryzhkov et al, 2005)
One degree beam – scan 3rpm: prf 1kHz – fold velocity 25m/s.
One degree dwell - 48 pulses. Pulse length = 267m gate.
Number of independent samples increases as the rate of
reshuffling increases, i.e as Doppler width of the target increases.
Can calculate noise in ZDR & DP
(B&C, Eq. 6.142 and 6.143)

## Slide 16: Standard deviation of ZDR for  = 0.99, 0.98, 0.97 as a function of Doppler width. N=48
48 independent pulses
X Mod rain 0.7dB
X Stormy rain 0.4dB
 ZDR(dB)

1m/s
Dopp
width

3m/s
Normalised Doppler width = Dopp Width/2*folding vely
Antenna imperfections and sidelobes can make the errors worse.
Remember values of ZDR often only 1dB
0.97
0.99
1dB
QUESTION: How does this noise affect
estimates of R?

## Slide 17: Standard deviation in DP for  = 0.97, 0.98, 0.99 as a function of Doppler width. N=48
x 3 in stormy weather
X 5 in mod rain

1m/s

2.5m/s
Normalised Doppler width
 DP()
KDP is the gradient of  DPwith range.
Differentiating noisy DP signal
gives an even noisier K DP.
QUESTION:
KDP of 1deg/km is about 55mm/hr
Can we measure if that if DP so noisy?

## Slide 18
Non uniform beam filling: can give –ve KDP!
Suppose initial DP= 0
Heavy precip (say) on left
Side of beam   DP= 40.
Further out, precip (say)
right side of beam,
unaffected by propagation
DP <40  K DP <0???
(X-band: from Gosset J Tech, 2004)

## Slide 19: 4. Use of ZDR & KDP:DP for more accurate rainrates.
THREE APPROACHES:
PHYSICAL – Calculate R as a function of Z, ZDR and KDP from analytical expressions for theoretical rain drop size spectra.
EMPIRICAL – Calculate values of Z, ZDR, KDP and R for many observed rain drop size spectra – find relationships to predict R by a best fit.
SYNTHETIC - Adjust relationship between R and Z, ZDR, KDP so that there is best agreement between the radar and the gauge totals.
QUESTION: Which method do you expect to be best in practice?

## Slide 20: Drop shape model.
Early work assumed drops <0.6 mm were spherical, for larger drops the axial ratio decreased linearly with drop size, with slope .
In 1982, to make radar observed ZDR agree with disdrometer, Goddard et al proposed that drops <4mm were more spherical.
In 1999, lab experiments by Andsager et al., confirmed that this empirical adjustment of drop shapes was essentially correct.
Values of ZDR and KDP using
Andsager et al., or Goddard et al.
drop shapes are essentially
identical – use these from now on.
Linear model predicts different ZDR,
KDP, and rain rates.
A recent approach is to have  as
a ‘free’ variable – i.e. drop shapes
vary (with turbulence?)
QUESTION: is this a good idea?

## Slide 21: Heavy convective rain: R from KDP|DP
PHYSICAL – Assume that the raindrop spectra are an exponential, but with rather fewer large drops (i.e. gamma function with =5):
e.g. R = 50.1 KDP0.7 (Illingworth and Blackman, JAM, 2002).
EMPIRICAL – fit from many observed spectra;
e.g. R = 50.7 KDP0.866 (B&C, 2001, CUP).
SYNTHETIC - Ryzhkov et al, (BAMS, 2005).
R = 44.0 |KDP| 0.822 sign(KDP)
Negative KDP values gives negative rainfall.
hail
But clearly ‘SYNTHETIC’ KDP is valuable in hail, when high Z gives big overestimate of R.
QUESTION:Can you average out the
negative rainfall to give net positive?

## Slide 22: Effect of noise on R from KDP|DP
Typical relationship: R = 50.7 KDP 0.866
So a KDP of 1deg/km is equivalent to 50.7mm/hr.
If (DP) = 3 or 5 then how accurate can we estimate KDP?
For N gates with a total path of L km use least squares fit to find KDP:
and its error (KDP) (B&C, Eq 6.155)
NEXRAD scan rate, 9 gates of 267m (L=2.4km) and
‘stormy weather’ (DP) = 3 then (KDP) = 0.72/km  37mm/hr
Use 25 gates, L=6.6km, for ‘lighter’ rain with lower Doppler width?
(DP) = 5 then (KDP) = 0.26/km  16mm/hr accuracy
but averaging over 6.6km  unacceptable loss of spatial accuracy?
CONCLUDE: KDP, noisy but BAMS (Ryzhkov et al., 2005)
article shows improved R from KDP in hail.
QUESTION: What is the minimum R for which KDP is useful?

## Slide 23: Rainfall from Z and ZDR
PHYSICAL – Assume exponential spectrum: N(D) = N0 exp(-3.67D/D0)
For No = 4224 m-3 mm-1 this gives Z = 300 R1.5.
Close to Nexrad: Z = 300 R 1.4 or R = 0.072 Z0.714.
BLACK LINE: Calculate Z and ZDR as D0 increases for R = 0.5 to 80mm/hr
If D0 is const then so is ZDR.
i.e assume shape of spectra constant.
2. Scaling Z (keeping ZDR constant) implies same scaling of N0 & R
i.e. R = a Z f(ZDR)
(Illingworth and Blackman, JAM 2002)
f(ZDR) decreases as ZDR increases – larger mean drop size.
Note spread in ZDR for 0.6dB noise
QUESTION: What does ZDR<0dB mean?

## Slide 24: Rainfall from Z and ZDR
PHYSICAL – Assume exponential spectrum: N(D) = N0 exp(-3.67D/D0)
Suppose No=4224 m-3 mm-1 this gives Z = 300 R1.5. {nexrad Z=300R1.4}
BLACK line Z=300 R1.5 + Suppose 0.6dB scatter in ZDR
If ZDR const, then so is D0, and Z scales with N0 and N0 fixes ‘a’
1. Averaging over 4 x 267m gates
gives resolution  1km by 1km
Halves errors to 0.3dB.
2. R = 1 and 10mm/hr can still
have the same ZDR.
ZDR can still go negative.
SOLUTIONS?
Scan more slowly? No
Need scan every 2.5mins.
2. Use Zdr in linear units so always
>0 & hope problem goes away?
3. Use scatter of Z and ZDR over
a region to fix ‘a’ in Z = a R1.5?
AND ALSO ERROR IN ‘a’
AND RAIN RATE
zdr(lin) 0.3 1.0

## Slide 25: Scatter of Z and ZDR from J-POLE
‘Tropical Rain’:
Noise in ZDR so values down to -0.4dB
High drop concentration,
ZDR is only 1dB for Z=50dBZ
‘a’ in Z = a R1.5 is low.
‘Rain mixed with hail’
Can’t use Z/ZDR retrieval
Need to recognize hail.
(From Ryzhkov et al. BAMS, 2005)
QUESTION: How do you really know if its hail?

## Slide 26: Rainfall from Z and ZDR
PHYSICAL – Assume exponential or well defined spectrum. R = a Z f(ZDR)
once ZDR is known, then R and Z scale with concentration N0.
EMPIRICAL Calculate R, Z and ZDR from drop spectra - best fit.
‘to avoid errors when ZDR tends to 0dB’ use linear Zdr = ZH/ZV
e.g. R = 0.0067 Z0.93 Zdr(lin) -3.43 (B & C, Table 8.1)
Note: Z0.93 implies shape of drop spectra changes systematically with R.
- this formula still gives rainfall >0 when ZDR is <0dB.
SYNTHETIC To give best agreement with gauges.
R = R(Z) / {0.4 + 5.0 | Zdr -1|1.3} (Ryzhkov et al, BAMS, 2005, eq A2)
where R(Z) = 0.0172 Z 0.714: standard NEXRAD.
Note that if Zdr(lin) = 1, then R = 2.5 (R(Z)),
but when Zdr(lin )<1 (ZDR –ve in dB) then R < 2.5 (R(Z)).
QUESTION: What does the use of | Zdr -1| mean physically?
FOR ALL THESE METHODS Z MUST BE CALIBRATED TO 0.5dB

## Slide 27: Calibration of Z using redundancy of Z, ZDR and KDP in rain.
By coincidence the ratio of KDP//ZH in rain is a unique function of ZDR which is relatively insensitive to changes in the shape of the drop spectrum.
Wrong ‘linear’ drop
shapes
O – exponential =0
X - gamma  = 5.
METHOD:
At each gate observe Z and ZDR and calculate theoretical KDP
From theoretical K DP find the DP at each gate.
Add up all DP to give total DP and compare with observed DP
Adjust Z so that they agree.

## Slide 28: CALIBRATION EXAMPLE
Observed total phase shift along ray is 25.
Adjust Z, so that phase shift calculated from observed
Z and ZDR agrees with observed phase shift.
Can calibrate Z to 0.5dB,
Use lots of rays to check.
If redundancy fails then
this suggests hail is in
the beam – use KDP to
calculate the rainfall.
Advantage:
Avoids the use of the noisy
observed value of K DP
Heavy rain

## Slide 29: Rainfall from KDP and ZDR
R (KDP, ZDR) = a KDPa ZDRb
has been proposed – where does it come from?
PHYSICAL – KDP is proportional to the difference in the forward scattering amplitudes at horizontal and vertical polarisation.
If drop shape  drop size, then the difference in amplitude  mean size,
and total amplitude is  liquid water volume (LWV) = ( N(D) D3 dD,
leading to KDP  D0 LWV (B&C, Eq 7.18)
Now, R  ( N(D) D3.67 dD and LWV  ( N(D) D3 dD
Integrating over an exponential size distribution gives us R = LWV 4.67/4
D0 is related to ZDR so we have: R (KDP, ZDR) = a KDPa ZDRb (B & C, Eq 8.17)
to avoid large errors as ZDR in dB approaches zero, express in linear Zdr
EMPIRICAL R(KDP, ZDr) = 90.8 KDP0.93 Zdr-1.69 (B&C, Table 8.2)
(from fits of R, KDP and ZDR calculated from rain spectra)
QUESTION: HAS THIS REALLY BEEN VALIDATED?
SYNTHETIC To give best agreement with gauges for R>6mm/hr:
R = R(KDP) / {0.4 + 3.5 | Zdr -1|1.7} (BAMS, 2005, Eq A3)
where R(K DP)=44.0 |KDP|0.822 sign(KDP) - PHYSICAL JUSTIFICATION?
QUESTION: Does this work for hail? KDP unaffected by hail, but ZDR values are unreliable in hail – empirical fits from raindrop spectra?
Does it seem bold to throw away Z for R > 6mm/hr?

## Slide 30: 5. Unwanted Backscatter and attenuation effects.
S-BAND
Mie scattering by large oblate hydrometeors. Envisage this as the H and V dipoles being displaced in space. This leads to:
  phase shift on backscatter – causes a local max (), in DP
  Lower correlation and so increased noise in the estimates.
  Lower correlation can help to identify large hail.
Solution – smooth the  DP to remove .
  For high ZDR rain, Z DR  , so use value of Z DR to remove .
Attenuation can be significant in very heavy rain. Oblate drops so more attenuation in H than V, decreases ZDR, can even go <0dB.
Solution. Attenuation is related to  DP .
e.g. Z(dB) = 0.04  DP () and Z DR (dB)= 0.004 DP ().
(Ryzhkov and Zrnic, JAM, 1995, and see B & C, table 7.1)
Question. This assumes that wet tumbling hail which gives no DP, does not attenuate Z. Does this matter?

## Slide 31: Use of C and X band.
C-BAND (5.6cm)
Widespread in Europe, Canada, Japan.
Antenna diameter halved – so volume/cost down by eight.
Attenuation by rain about ten times worse than S-band.
Solution – use DP to correct for attenuation.
Z(dB) = 0.073 DP () & Z DR(dB)= 0.013 DP (). (B&C, Table 7.1)
  Remember attenuation varies with temp, phase shift does not.
  Also Mie scattering (big drops, high ZDR) give more attenuation.
  Big drops, high Z DR  , so use value of Z DR to remove .
X-BAND (3cm) – ‘cheap’ fill-in radars for NEXRAD?.
Attenuation enormous, 1.4dB/km 2-way for 30mm/hr and f(Temp).
Use phase shift to correct for (say) 20dB of attenuation? Careful!
DP  frequency, so KDP.is larger. OK for lower rain rates?
 on backscatter worse. (Scott et al, J Tech, 2001). Suggested correction: =0.027ZDR+0.77ZDR2 (Gosset, J Tech, 2004)
Area of active research. QUESTION: IS THIS REALLY A GOOD IDEA?

## Slide 32: 5. SUMMARY
Polarisation good for rejecting non-meteorological echoes.
S-BAND – Summer convective storms.
Precipitation signals are noisy for operational radars.
Differential phase shift, KDP does not respond to hail, and gives improved rainfall rates (for high R) when hail is present.
The status of algorithms deriving R from KDP and ZDR is uncertain. KDP is noisy, ZDR is affected by hail.
Z and ZDR should yield better value of R than from Z alone.
Cannot use ZDR at each gate – can go negative.
Use scatter of Z and ZDR to fix N0 and hence ‘a’ in Z = aR1.5
Need to recognise hail and calibrate Z to better than 1dB.
The redundancy of Z, Z DR and K DP in rain should enable Z to be absolutely calibrated and hail to be recognised.
Winter time – bright band and vertical profile correction schemes.
Polarisation parameters can recognise melting snow and flag the high Z values in the bright band.